## Slide 1
ESP-NOW Overview and Implementation

## Slide 2
What is ESP-NOW
Two ESP8266 ESP-NOW Implementation
Three ESP8266 ESP-NOW Implementation
Battery Powered Considerations
Summary

## Slide 3
ESP-NOW is a kind of connectionless WiFi communication protocol which is defined as Espressif.
What is ESP-NOW ?

## Slide 4
{"mailbox":{"description": "mailbox opened","supply":3032,"deviceid":18040501}}
Two ESP8266 ESP-NOW Implementation

## Slide 6
{“Enviro":{"temp":78.6,"humidity":29,"supply":3041,"deviceid":18040501}}
Three ESP8266 ESP-NOW Implementation

## Slide 8
Power Drain Considerations
 | Deep Sleep | Sending Data
All Components | 19.8 mA | 134 mA
Remove Regulator | 16.3 mA | 116 mA
Disconnected UART | 21 uA | 86 mA
Calculations:
Battery: 1000mAh
Deep Sleep
1000mAh/.021mA ~ 2k days (~ 5 years)
Sending Data
Tx(s) < 1sec
[1000mAh/(86mA)] * (3600s/1h) = 42k-sec
Assume 4 cycles/day (~ 28 years)

## Slide 9
Summary/Discussion